## Slide 1
Energy
Wind Turbine

## Slide 2
HISTORY
The first wind-mills were developed in Persia and probably in Chaina between 500-900 B.C to automate the tasks of water-pumping and grain grinding .
From there the use of wind-mills spread from Persia to the surrounding areas in the middle east , where it was used in food production.
Around 1,000 A.D., wind power technology spread north to European countries such as The Netherlands, which adapted windmills to help drain lakes and also to grind grain, with a new design for the wind mill – a tower mill.
The technology developed between 1850 and 1970, over six million mostly small (1 horsepower or less) mechanical output wind machines were installed in the U.S. alone.

## Slide 3
INTRODUCTION
Wind energy is created when the atmosphere is heated unevenly by the Sun, some patches of air become warmer than others. These warm patches of air rise, other air rushes in to replace them thus, wind blows.
Wind turbine is a device that converts kinetic energy from the wind into electric power.
It works opposite of fan turbine blade spin from the wind and make energy instead of using energy to make wind.
The first windmill used to produce electric energy was created in 1888 by Charles F. Brush.
The wind power programme in India was started during 1983-84 with the efforts of the Ministry of Non-Conventional Energy Sources.

## Slide 4
Components of wind turbine

## Slide 5
Function of Component
Foundation: Foundation give support to wind turbine. It consist of solid concrete assembly
Tower : It connect rotor and foundation and raise rotor so that it can operate at required wind. Made up of steel having tube like structure.
Nacelle : Contains the key components of the wind turbine including the gearbox , yaw system and electric generator
Rotor & Rotor blades : It is rotating part which converts wind energy to rotation. It is made up of glass-fibre, carbon-fibre, reinforced plastics.
Low speed shaft: Connects the rotor hub to the gearbox.
High speed shaft : Drives the electrical generator by rotating at high speed.

## Slide 6
Function of Component
Gearbox :- The gearbox converts the rotor motion of lower rpm into the higher rpm.
Coupling :- Coupling is done between the main shaft and the transmission.
Generator :- Generates electricity from rotation of shaft.
Controller :- It is a self operating system use in control system. It may be sensor (mechanical, electrical),
decision elements( relays, microprocessor) and actuators( hydraulic, electric).
Yaw mechanism :- Turns the nacelle with the rotor into the wind using motors.
Anemometer and wind vane :- Measures the speed and the direction of the wind while sending signals to
the controller to start or stop the turbine.

## Slide 7
Working

## Slide 8
Types of wind turbine
Horizontal axis type
A horizontal axis machine has its blades rotating on an axis parallel to the ground.
Single blade Horizontal wind turbine | Two blades Horizontal wind turbine | Three blades Horizontal wind turbine
Lower blade weight and less cost.
More vibration & unconventional look.
Similar to single blade HAWT.
Have stability problem
  increases gearbox costs
Balance of gyroscopic forces

## Slide 9
Types of wind turbine
Vertical axis type
Darrieus wind turbine | Savonius wind turbine
Vertical axis wind turbines(VAWTs) have the main rotor shaft arranged vertically.
VAWTs runs in any wind direction.
Good efficiency
Produce large torque and cyclic stress on the tower
Require some external power source to start turning
drag type turbine
self starting
less efficient
used in cases of high reliability in many things such as ventilation and anemometers.

## Slide 10
Size of wind turbine
Small (10 kW)
Homes
Farms
Remote Applications
(e.g. water pumping, telecom sites,)
Large (250 kW - 2+MW)
Central Station Wind Farms
Distributed Power
Intermediate
(10-250 kW)
Village Power
Hybrid Systems
Distributed Power

## Slide 11
Are they worth it, energy-wise?
Energy and Sustainability
Small scale wind turbines
Notes: Wind power was very popular in the search for renewable energy sources, it is quite developed.
What was interesting to me was to see what will happen if we use small scale wind turbines in our homes. What will be the influence.
No cover for financial information

## Slide 12
Horizontal axis wind turbine (HAWT)
Vertical axis wind turbine (VAWT)
Types of small-scale wind turbines
Anemometer
Notes: The most common type in the UK is the HAWT [Bahaj et al., (1)]

## Slide 13: HAWT
Main rotor shaft and electrical generator at the top of the tower
Must be pointed into the wind
Main rotor shaft arranged vertically
The generator and gearbox can be placed near the ground
Does not need to be pointed into the wind
Relatively low rotational speed
VAWT
Types of small-scale wind turbines
Notes: Most of the small scale (and in general) wind turbines are horizontal axis – more efficient, usually
Most early ones – vertical
In Europe - horizontal

## Slide 14
– rotor diameter
– air density
– wind velocity
[Sahin et al. 2006]
Gross power small scale wind turbines
Notes: Wind turbine - a device that converts kinetic energy from the wind into electrical power.
U (cubic) and D (square) are the dominant factor
Has cubic dependence on wind velocity

## Slide 15: Betz limit - Max power of
[Betz 1946]
Power limit small scale wind turbines
Notes: 16/27 or 59% of the Gross power. Betz's law calculates the maximum power that can be extracted from the wind.
Real turbine extract less than Betz limit due to aerodynamics and power conversion losses.
Figure: representative micro-wind turbine power curve, compared with the Gross power and the Betz limit.

## Slide 16
[Entec]
Power curve small scale wind turbines
Notes: Entec – a company that de sign environmental solutions and products
http://www.entec-international.com/
Cut-in speed: At very low wind speeds, there is insufficient torque exerted by the wind on the turbine blades to make them rotate
Rated power: the power output reaches the limit that the electrical generator is capable of – keep the power at const level
Cut-out speed: There is a risk of damage to the rotor

## Slide 17
[Entec]
Wind resource small scale wind turbines
Notes: Globally, winds are caused by pressure gradients generated by the differential heating of the Earth’s surface by the Sun
Within the atmospheric boundary layer the shear stresses caused by the Earth’s surface extract momentum from the wind,
and cause a variation of velocity with height. Topography,surface roughness etc.
Urban environments typically have the greatest surface roughness, and climatological processes in such environments are accordingly complex.

## Slide 18
[Roth, 2000]
Turbulence small scale wind turbines
Rated power of less than 50kW
Notes: Turbulence intensity as a function of height in urban environments

## Slide 19
[Carbon trust]
Comparison small scale wind turbines
 | micro HAWT | Swift rooftop wind turbine
Power rating (kW) | 0.6 | 1.5
Mean annual output (kWh) | 870-164 | 2000 - 3000
Rotor diameter (m) | 1.7 | 2
Lifetime (y) | 15 | 20
Rated velocity (m/s) | 12 | 12
Notes: 1650/2.5 = 660
4300/3.3 = 1303
1900/1.4 = 1360

## Slide 20
The performance of wind turbines depend on 5 major factors:
WIND POWER
AIR
TEMPERATURE
BLADE
AERODYNAMICS
OBSTRUCTIONS
ALTITUDE

## Slide 21
Site Selection
Consideration during site selection
High annual average wind speed
Altitude of proposed site
Terrain and aerodynamic
Ease of transportation
Nearness to users/centers
Best sites for wind turbine
Off shore and sea coast (2400 kWh/ per year)
Mountains (1600 kWh/ per year)
Planes (750 kWh/ per year)
Local ecology & Nature of ground

## Slide 22
Wind farms
A wind farm or wind park is a group of wind turbines in the same location used to produce energy.
Offshore wind farms
Wind farm located right off the
coast or in sea using floating platform.
More wind power but more cost.
Onshore wind farms
Less wind power available than offshore.
Less cost in installation.
Usually near to user but create noise and visual problems.
Jaisalmer wind park, Rajasthan (1064 MW)
London Array, United Kingdom (630 MW)

## Slide 23
Location of wind farm
Worldwide there are now over two hundred thousand wind turbines operating, with a total nameplate capacity of 318,105 MW.
Top 10 countries by nameplate wind power capacity
wind energy installations in states across India

## Slide 24
Safety System
Emergency stop :- If a situation arises which calls for the wind turbine to be stopped immediately, it is
used and wind turbine stop in few seconds by feathering the blade directly into the wind.
Computer and sensors :- The wind turbine is controlled by a computer and data from sensors
which monitors the most important gauging instrument and compare the result , if
found error wind turbine is stopped.
Lightning Rods :- The wind turbine system is protected from lighting by these rods going from the tip
of the blade to the ground.
Temporary Rope System :- This system provides temporary fall protection during construction,
maintenance or inspection of wind turbine.

## Slide 25
ADVANTAGE
Good for environment as it uses renewable source of energy as wind.
Wind is freely available in nature.
Can be setup in remote areas where electricity through transmission wire cannot be reached.
Clean source of energy as it does not produce any green house gases or any other pollutants.
Once setup is completed the cost of generation electricity become less.
Can be combined with solar electricity to give reliable supply of electricity.
Cost comparison of different sources |  | 
Power plant type | Cost ($/kW-hr) | Renewable sources
Natural gas | 0.07-0.13 | No
Hydro | 0.08 | Yes
Coal | 0.08-0.14 | No
Wind | 0.08-0.15 | Yes
Nuclear | 0.10 | No
Biomass | 0.10 | Yes
Solar PV | 0.13 | Yes
Chart: CO2 Emissions of diff. Power Sources per Electric-generating Capacity
| Hydro | Nuclear | Wind | Solar PV | Natural gas fired | coal fired
CO2 emission(g-CO2/kWh) | 11 | 20 | 25 | 38 | 738 | 943

## Slide 26
DISADVANTAGE
Site Specific i.e suited to particular region.
Create a lot of Noise Disturbances
Prediction of wind is difficult i.e wind speed varies.
Threat to wild life as it kills birds.
Cause visual impact.
High Initial cost.
Large requirement of land for wind farm.
Turbines Interfere With the Reception of Televisions and communication signals.

## Slide 27
Future
Price of wind power is coming down.
Technological Developments as application specific Turbines
Offshore
  Limited land/resource areas
  Transportation or construction limitations
  Low wind resource
  Cold climates
Wind farms can provide a surplus of reliable clean energy to society.
Can become cost competitive for electricity generation if fossil energy costs skyrocket.
Wind alone can not solve today’s energy crisis in one day, but together with many other forms of renewable power, maybe someday we can help relieve the damage to our planet caused by the overconsumption of fossil fuels.